# HEXADECIMAL TO DECIMAL
# AIM
# To develop an assembly language program to convert a number in Hexadecimal to it’s decimal equivalent.
# ALGORITHM
# Algorithm 1 Hex to decimal conversion
# 1: Start
# 2: Read the input in hexadecimal (hex).
# 3: m = hex/A
# 4: d ec = hex + 6 ∗ m
# 5: Print the result in decimal (d ec).
# 6: Stop
# SOURCE CODE
# mov a , r0
# mov b,#0ah
# div ab
# mov b,#06h
# mul ab
# add a , r0
# mov r1 , a
# stop: sjmp stop
# INPUT:
# Input in R0
# OUTPUT:
# Output in R1

RESULT:
Assembly language program for converting a number in hexadecimal to it’s equivalent decimal has been developed and verified using MCU-8051-IDE.

# SACHIN G
# RO:54