# DECIMAL TO HEXADECIMAL
# AIM
# To develop an assembly language program to convert a number in decimal to it’s equivalent Hexadecimal.
# ALGORITHM
# Algorithm 1 Decimal to hex conversion
# 1: Start
# 2: Read the input in decimal (d ec).
# 3: m = d ec/16
# 4: hex = d ec − 6 ∗ m
# 5: Print the result in hexadecimal (hex).
# 6: Stop
# SOURCE CODE
# MOV A , R0
# MOV B,#10H
# DIV AB
# MOV B,#06H
# MUL AB
# MOV R1 , A
# MOV A , R0
# SUBB A , R1
# MOV R1 , A
# STOP: SJMP STOP
# INPUT:
# Input in R0
# OUTPUT:
# Output in R1

RESULT:
Assembly language program for converting a number in decimal to it’s equivalent hexadecimal has been developed and verified using MCU-8051-IDE.

# SACHIN G
# RO:54