# POSITIVE OR NEGATIVE
# AIM
# To develop an assembly language program to check whether the given number is positive or negative.
# ALGORITHM
# Algorithm 1 Check whether given number is positive or negative
# 1: Start
# 2: Read the input (n).
# 3: Let n i be the MSB of n.
# 4: if n i = 1 then
# 5: print "The number is negative"
# 6: else
# 7: else
# 8: end if
# 9: Stop
# SOURCE CODE
# ORG 0000H
# MOV A, R7
# RLC A
# JC neg
# MOV B,#00H ;if positive then 0 else 1
# SJMP last
# neg:MOV B,#01H
# last:END
# OUTPUT:
# Output with R7 = 10H
# Output with R7 = F2H

RESULT:
Assembly language program to check whether a given number is positive or negative has been developed and verified using MCU-8051-IDE.

# SACHIN G
# RO:54