# SMALLEST AND LARGEST
# AIM
# To develop an assembly language program to find the largest and smallest of 8-bit numbers.
# ALGORITHM
# Algorithm 1 Largest and smallest of 8-bit numbers
# 1: Start
# 2: Read the size of array (n).
# 3: Read the array (arr).
# 4: max = arr [0]
# 5: mi n = arr [0]
# 6: for i = 1 to (n− 1) do
# 7: if arr[i]>max then
# 8: max = arr[i]
# 9: else if arr[i]< mi n then
# 10: min = arr[i]
# 11: end if
# 12:end if
# 13:Print largest (max) and smallest (min) of the numbers.
# 14:Stop
# SOURCE CODE
# ORG 0000H
# MOV R0, #030H ;Start address of array
# MOV R7,#04H ;number of elements
# MOV A,@R0 ;smallest stored in R1
# MOV R1,A
# MOV B,@R0
# MOV R2,B ;largest stored in R2
# INC R0
# Find:DJNZ R7,next
# JMP END
# next:CLR C
# MOV A,R1
# SUBB A,@R0
# JNC small ;a is small
# JMP check
# small:MOV A,@R0
# MOV R1,A
# check:CLR C
# MOV A,R2
# SUBB A,@R0
# JC large
# JMP finish
# large:MOV A,@R0
# MOV R2,A
# finish:INC R0
# JMP find ;smallest in R1 ,largest in R2
# END: END
# INPUT:
# Input at addresses starting from 0x30
# OUTPUT:
# Smallest in R1 and Largest in R2

RESULT:
Assembly language programs for finding the largest and smallest of 8-bit numbers have been developed and verified using MCU-8051-IDE.

# SACHIN G
# RO:54